## Slide 1
Data and Signals

## Slide 2
To be transmitted, data must be transformed to electromagnetic signals.
Note

## Slide 3
3-1 ANALOG AND DIGITAL
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. Analog data take on continuous values. Digital data take on discrete values.
Analog and Digital Data
Analog and Digital Signals
Periodic and Nonperiodic Signals
Topics discussed in this section:

## Slide 4: Analog and Digital Data
Data can be analog or digital.
Analog data are continuous and take continuous values.
Digital data have discrete states and take discrete values.

## Slide 5: Analog and Digital Signals
Signals can be analog or digital.
Analog signals can have an infinite number of values in a range.
Digital signals can have only a limited number of values.

## Slide 6
Figure 3.1 Comparison of analog and digital signals

## Slide 7
3-2 PERIODIC ANALOG SIGNALS
In data communications, we commonly use periodic analog signals and nonperiodic digital signals.
Periodic analog signals can be classified as simple or composite. A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals. A composite
periodic analog signal is composed of multiple sine waves.
Sine Wave
Wavelength
Time and Frequency Domain
Composite Signals
Bandwidth
Topics discussed in this section:

## Slide 8
3-2 PERIODIC ANALOG SIGNALS

## Slide 9
Figure 3.2 A sine wave

## Slide 10
Figure 3.3 Two signals with the same phase and frequency, but different amplitudes

## Slide 11
Frequency and period are the inverse of each other.
Note

## Slide 12
Figure 3.4 Two signals with the same amplitude and phase, but different frequencies

## Slide 13
Table 3.1 Units of period and frequency

## Slide 14
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:
Example 3.1

## Slide 15
The period of a signal is 100 ms. What is its frequency in kilohertz?
Example 3.2
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).

## Slide 16: Frequency
Frequency is the rate of change with respect to time.
Change in a short span of time means high frequency.
Change over a long span of time means low frequency.

## Slide 17
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.
Note

## Slide 18
Phase describes the position of the waveform relative to time 0.
Note

## Slide 19
Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases

## Slide 20
A sine wave is offset 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Example 3.3
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is

## Slide 21
Figure 3.6 Wavelength and period

## Slide 22
Figure 3.7 The time-domain and frequency-domain plots of a sine wave

## Slide 23
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.
Note

## Slide 24
The frequency domain is more compact and useful when we are dealing with more than one sine wave. For example, Figure 3.8 shows three sine waves, each with different amplitude and frequency. All can be represented by three spikes in the frequency domain.
Example 3.7

## Slide 25
Figure 3.8 The time domain and frequency domain of three sine waves

## Slide 26: Signals and Communication
A single-frequency sine wave is not useful in data communications
We need to send a composite signal, a signal made of many simple sine waves.
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases.

## Slide 27: Composite Signals and Periodicity
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies.
If the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies.

## Slide 28
Figure 3.9 shows a periodic composite signal with frequency f. This type of signal is not typical of those found in data communications. We can consider it to be three alarm systems, each with a different frequency. The analysis of this signal can give us a good understanding of how to decompose signals.
Example 3.4

## Slide 29
Figure 3.9 A composite periodic signal

## Slide 30
Figure 3.10 Decomposition of a composite periodic signal in the time and frequency domains

## Slide 31
Figure 3.11 shows a nonperiodic composite signal. It can be the signal created by a microphone or a telephone set when a word or two is pronounced. In this case, the composite signal cannot be periodic, because that implies that we are repeating the same word or words with exactly the same tone.
Example 3.5

## Slide 32
Figure 3.11 The time and frequency domains of a nonperiodic signal

## Slide 33: Bandwidth and Signal Frequency
The bandwidth of a composite signal is the difference between the highest and the lowest frequencies contained in that signal.

## Slide 34
Figure 3.12 The bandwidth of periodic and nonperiodic composite signals

## Slide 35
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.6
The spectrum has only five spikes, at 100, 300, 500, 700, and 900 Hz (see Figure 3.13).

## Slide 36
Figure 3.13 The bandwidth for Example 3.6

## Slide 37
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.7
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.14).

## Slide 38
Figure 3.14 The bandwidth for Example 3.7

## Slide 39
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure 3.15 shows the frequency domain and the bandwidth.
Example 3.8

## Slide 40
Figure 3.15 The bandwidth for Example 3.8

## Slide 41
An example of a nonperiodic composite signal is the signal propagated by an AM radio station. In the United States, each AM radio station is assigned a 10-kHz bandwidth. The total bandwidth dedicated to AM radio ranges from 530 to 1700 kHz. We will show the rationale behind this 10-kHz bandwidth in Chapter 5.
Example 3.9

## Slide 42
Another example of a nonperiodic composite signal is the signal propagated by an FM radio station. In the United States, each FM radio station is assigned a 200-kHz bandwidth. The total bandwidth dedicated to FM radio ranges from 88 to 108 MHz. We will show the rationale behind this 200-kHz bandwidth in Chapter 5.
Example 3.10

## Slide 43
Another example of a nonperiodic composite signal is the signal received by an old-fashioned analog black-and-white TV. A TV screen is made up of pixels. If we assume a resolution of 525 × 700, we have 367,500 pixels per screen. If we scan the screen 30 times per second, this is 367,500 × 30 = 11,025,000 pixels per second. The worst-case scenario is alternating black and white pixels. We can send 2 pixels per cycle. Therefore, we need 11,025,000 / 2 = 5,512,500 cycles per second, or Hz. The bandwidth needed is 5.5125 MHz.
Example 3.11

## Slide 44: Fourier Analysis
Fourier analysis is a tool that changes a time domain signal to a frequency domain signal and vice versa.
Note

## Slide 45: Fourier Series
Every composite periodic signal can be represented with a series of sine and cosine functions.
The functions are integral harmonics of the fundamental frequency “f” of the composite signal.
Using the series we can decompose any periodic signal into its harmonics.

## Slide 46: Fourier Series

## Slide 47: Examples of Signals and the Fourier Series Representation

## Slide 48: Sawtooth Signal

## Slide 49: Fourier Transform
Fourier Transform gives the frequency domain of a nonperiodic time domain signal.

## Slide 50: Example of a Fourier Transform

## Slide 51: Inverse Fourier Transform

## Slide 52: Time limited and Band limited Signals
A time limited signal is a signal for which the amplitude s(t) = 0 for t > T1 and t < T2
A band limited signal is a signal for which the amplitude S(f) = 0 for f > F1 and f < F2

## Slide 53: Fourier Series Recap

## Slide 54
Some Math

## Slide 65: Fourier Series Recap

## Slide 66: Fourier Series

## Slide 71: Recap formulas

## Slide 75: Exercises

## Slide 83: Exercise 2