## Slide 1: CSE 201: Digital Logic Design
Prepared By
Lec Sumaiya Afroz Mila
CSE, MIST

## Slide 2: BINARY ADDER
The most basic arithmetic operation is the addition of two binary digits.
A combination circuit that performs the addition of two bits is half adder
A adder performs the addition of 2 significant bits and a previous carry is called a full adder

## Slide 3
x y | C S
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
x
+ y
───
C S
Half Adder
  Adds 1-bit plus 1-bit
  Produces Sum and Carry
BINARY ADDER

## Slide 4: BINARY ADDER
x y z | C S
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
x
+ y
+ z
───
Cout S
Full Adder
  Adds 1-bit(x) plus 1-bit(y) plus 1-bit(z)
  Let the bit z be the carry-in bit
  Produces Sum and Carry Out

## Slide 5: BINARY ADDER
For the combination x=1, y=1 and z=1
─ If we perform the addition operation without considering the input carry (z bit)
─ If we perform the addition operation considering the input carry (z bit)
x y z | C S
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
1
+ 1
───
Cout S
1 0
1
+ 1
1
───
Cout S
1 1

## Slide 6
4- bit Parallel Adder using Full Adders
1 0 1 1
0 0 1 1
0
1
1
1
1
1
0
0
Ai Bi Ci | Ci+1 Si
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1

## Slide 7
  c4 c3 c2 c1 c0
  + A3 A2 A1 A0
  + B3 B2 B1 B0
  ────────────
4- bit Parallel Adder using Full Adders
S0
S1
S2
S3
C1
C2
C3
C4
C4
1 0 1 1
0 0 1 1
0
1
1
1
1
1
0
0

## Slide 8
FA
FA
FA
FA
Carry Propagate Addition
4- bit Parallel Adder using Full Adders
  c4 c3 c2 c1 c0
  + A3 A2 A1 A0
  + B3 B2 B1 B0
  ────────────
S0
S1
S2
S3
C1
C2
C3
C4
C4
C0=0
A0
B0
S0
C1
A1
B1
S1
C2
A2
B2
S2
C3
A3
B3
S3
C4

## Slide 9
FA
FA
FA
FA
4- bit Parallel Adder using Full Adders
  0 0 1 1 0
  + 1 0 1 1
  + 0 0 1 1
  ────────────
0
1
1
1
1
1
0
0
0
C0=0
1
1
0
1
1
1
1
1
0
0
1
0
1
0
1
0
Carry in
A
B
Sum
Carry out
S0
S1
S2
S3
C1
C2
C3
C4

## Slide 10
4- bit Parallel Adder Diagram
4-bit parallel adder
B3 B2 B1 B0
A3 A2 A1 A0
S3 S2 S1 S0
C0
C5
Input Terminals
Output Terminals

## Slide 11: BINARY SUBTRACTOR
The subtraction operation (A-B) can be done by (A+ 2’s complement of B)
  Take 1’s complement or invert of B
  Add A with 1’s complement of B
  Add 1 with the least significant bits of the previous addition
This can be achieved by modifying the n-bit parallel adder by
  adding an inverter in input of B
  Input carry C0 must be equal to 1
For unsigned numbers-
  This operation gives (A-B) if A ≥ B
  And 2’s complement of B-A if A≤B

## Slide 12
FA
FA
FA
FA
4- bit Parallel Subtractor using Full Adders
C0=1
A0
B0
S0
C1
A1
B1
S1
C2
A2
B2
S2
C3
A3
B3
S3
C4
A3 A2 A1 A0
+B’3B’2B’1B’0
+ 1

## Slide 13
4- bit Adder - Subtractor

## Slide 14: Limitations in Parallel Adder
All bits of addend and augend should be available for computation at the same time
Each bit of sum output depends on the value of the input carry
Similarly C3 has to wait for C2, and C2 has to wait for C1
Thus only after the carry propagates through all the stages, S4 will be in its steady state
When these 3 bits are available, sum bit S1 will be in steady state
For S2 to be in steady state, A2,B2 and carry C2 must be available
For S4 to be in steady state, A4,B4 and carry C4 must be available
Input A4 & B4 reach steady state as soon as input signals are applied to the adder
But C4 does not settle to its steady state until C3 is available

## Slide 15: Limitations in Parallel Adder
Carry propagation from C1 to C4 causes propagation delay
The signal from the input carry Ci to the output carry Ci+1, propagates through an AND gate+ an OR gate, means two gate levels.
C2 has 2 gate levels from C1 to C2
C3 has 2 gate levels from C2 to C3 and 4 gate levels from C1 to C3
Similarly, in the previous design with 4 full adders, C5 has 4*2=8 gate levels from C1 to C5
So, the total propagation time would be, propagation time in one half adder plus 8 gate levels

## Slide 16: Limitations in Parallel Adder
Carry propagation time is a limiting factor on the speed
Though the parallel adder will always have some value in the output terminals, outputs will not be correct unless signals are given enough time to propagate through the gates connected from the inputs to the outputs
One technique to reduce the carry propagation time is look-ahead carry

## Slide 17: LOOK-AHEAD CARRY
Output sum and carry can be expressed as:
Booelan Function for carry output of each stage:
C5 can be derived by the equation substitution method:
C5 = G4+P4C4
= G4 + P4(G3+P3G2+P3P2G1+P3P2P1C1)

## Slide 18: LOOK-AHEAD CARRY
Boolean function for each output carry is expressed in sum of products.
Each function can be implemented with one level of AND gate, followed by an OR gate.
Carry outputs depend on the variable P and G. Pi and Gi are functions of input Ai and Bi which are available as soon as inputs are applied to the adder.
In this design, C4 does not have to wait for C3 and C2 to propagate.
In fact, C4 is propagated at the same time as C3 and C2

## Slide 19: LOOK-AHEAD CARRY
C5 = G4+P4C4
= G4 + P4(G3+P3G2+P3P2G1+P3P2P1C1)
Connection of C5 is not shown here.
However, we can add the connection for C5

## Slide 20: 4-BIT FULL ADDERS WITH LOOK-AHEAD CARRY
Si = Pi xor Ci
S1 = P1 xor C1
S2 = P2 xor C2
S3 = P3 xor C3
S4 = P4 xor C4
we have to add the connection for C5 here
We can hide the complex circuit of Look-ahead carry and replace it with this box.

## Slide 21
4-BIT FULL ADDERS WITH LOOK-AHEAD CARRY
So, the new design can be drawn like this

## Slide 22: Logic Circuits
Logic Circuits: Combinational and Sequential
Combinational Circuits
  A combinational circuit consists of logic gates whose outputs at any time are determined from only the present combination of inputs.
Sequential Circuits
  A sequential circuits employ storage elements and logic gates.
  The outputs are a function of the inputs and the state of the storage elements.
  The state of the storage elements, in turn, is a function of the previous inputs (and the previous state).

## Slide 23: BINARY CODED DECIMAL
Binary coded decimal (BCD) is a system of writing numerals that assigns a four-digit binary code to each digit 0 through 9 in a decimal (base-10) numeral.
Numbers larger than 9, having two or more digits in the decimal system, are expressed digit by digit. For example, the BCD rendition of the number 1895, (base-10) is
Decimal | BCD | Binary
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0010
3 | 0011 | 0011
4 | 0100 | 0100
5 | 0101 | 0101
6 | 0110 | 0110
7 | 0111 | 0111
8 | 1000 | 1000
9 | 1001 | 1001
0001 1000 1001 0101

## Slide 24: BCD ADDER
We will perform addition operation of two decimal numbers in BCD
Each input does not exit 9
Sum output will be highest: 19
The binary value and BCD value of the augend and addend are same
Apply the BCD value of the augend and the addend to a 4-bit binary adder
Adder will form the sum in binary and produce a result that may range from 0 to 19
This binary result should be converted to BCD
9(augend)
+9(addend)
+1(input carry)
19

## Slide 25: BCD ADDER

## Slide 26: BCD ADDER
From the table, when binary sum ≤ 1001(910), corresponding BCD is identical – No conversion needed
When binary sum > 1001, it becomes non-valid as BCD – conversion needed
  For binary sum>1001, we have to convert it to a valid BCD representation
  When binary sum is 1010, decimal is 10 – correct BCD representation will be
  To convert 1010 to 10000, we have to add (0110)2 or (6)10 with 1010
  Similarly if we add (0110)2 or (6)10 with 1011……10011, we will get the corresponding BCD representation
0001 0000

## Slide 27: BCD ADDER
Now we have to design the circuit.
We have to design a circuit that will detect when conversion should be performed and when not.
From the table, it is
visible that, conversion
is needed when the
binary sum has an
output carry K=1.
Other 6 combinations
From 1010 to 1111 that
Need conversion have a 1 in position z8
To distinguish them form the value 1000 and 1001 (also have a 1 in position Z8), we specify, either Z4 or Z2 must have a 1
    C = K + Z8Z4 + Z8Z2
K Z8 Z4 Z2 Z1 C S8 S4 S2 S1

## Slide 28: BCD ADDER
    When C = K + Z8Z4 + Z8Z2 ,it is necessary to add 110 to the binary sum and provide an output carry for the next stage
    To add 0110 to the binary sum, we use a second 4-bit binary adder
    First the augend, added
    and the input carry are
    added in the top 4-bit binary adder
    to produce the binary sum
    When output carry=0 nothing
    added
    When output carry=1,binary 0110
    is added to the binary sum through the
    bottom 4-bit binary adder

## Slide 29
2- BIT by 2-BIT BINARY MULTIPLIER

## Slide 30: MAGNITUDE COMPARATOR
Magnitude Comparator: A magnitude comparator is a combinational circuit that compares two numbers A and B, and determines their relative magnitudes. The outcome of the comparison is specified by three binary variables that indicate whether A=B , A>B , or A<B
The circuit for comparing two n-bit numbers has 22n entries in the truth table and becomes too cumbersome even with n=3.
So, we will develop an algorithm to design a comparator

## Slide 31: MAGNITUDE COMPARATOR
We will consider two 4-bit numbers:
    A = A3A2A1A0
    B = B3B2B1B0
The two numbers are equal if all pairs of significant digits are equal. If A3=B3 & A2=B2 & A1=B1 & A0=B0
So the equality relation of each pair of bits will be
  xi = AiBi+Ai’+Bi’ , where xi=1 only if the pair of bits in position i are equal
If all pair of bits of A and B are equal which means, if X3X2X1X0 all are equal 1, we can say A=B

## Slide 32: MAGNITUDE COMPARATOR
1 0 1
1 1 1 1
To determine if A>B or A<B, we inspect relative magnitudes of significant bits starting from the MSB
If these two bits are equal, we compare the next lower significant pair of bits
This comparison continues until a pair of unequal digits is reached
    If the corresponding digit of A=1 and that of B=0, we conclude A>B
    If the corresponding digit of A=0 and that of B=1, we conclude A<B
The boolean function for the above sequential comparison will be:
A3 A2 A1 A0
B3 B2 B1 B0
1 1 1
1 1 0 1

## Slide 33: MAGNITUDE COMPARATOR
1 0 1
1 0 1 1
1 1 1
0 1 0 1
If A3B3’ = 1, A>B
If X3A2B2’ = 1, A>B
1 1 1
1 1 0 1
If X3X2A1B1’ = 1, A>B
A3 A2 A1 A0
B3 B2 B1 B0
1 1 1
1 1 1 0
If X3X2X1A0B0’ = 1, A>B

## Slide 34: MAGNITUDE COMPARATOR

## Slide 35: MAGNITUDE COMPARATOR
xi = AiBi+Ai’+Bi’
(A0’B0+A0B0’)’ = (A0 xor B0)’
            = A0 xnor B0
            = A0B0+A0’B0’

## Slide 36
A decoder is a combinational circuit that converts binary information from n-input lines to a maximum 2n unique output lines.
If the n-bit decoded information has unused or don’t care combinations, the decoder output will have fewer than 2n outputs
This decoders are called n-to-m-line decoders, where m ≤ 2n
1-to-2-Line Decoder -
DECODER

## Slide 37
The 2 inputs are decoded into 4 outputs
Each output represents one of the
minterms of the 2-input variables
2 intverters provide the complement of
the inputs
Each one of the 4 AND gates generate one
of the minterms
A B | D3 | D2 | D1 | D0
0 0 | 0 | 0 | 0 | 1
0 1 | 0 | 0 | 1 | 0
1 0 | 0 | 1 | 0 | 0
1 1 | 1 | 0 | 0 | 0
2-to-4 Line Decoder
D3
D2
D1
D0

## Slide 38
3-to-8 Line Decoder
3 inputs are decoded into 8 outputs
Each output represents
one of the minterms of the
3-input variables
3 intverters provide the
complement of the inputs
Each one of the 8 AND
gates generate one of the minterms

## Slide 39
3-to-8 Line Decoder
A particular application of this decoder
is binary-to-octal conversion.
The input variables represent
a binary number
The outputs represent the
eight digits of a number in
octal number system

## Slide 40
Some decoders are constructed with NAND gates
May include one or more Enable inputs to control the circuit operation
Circuit operates with complemented output
and complement enable input
The decoder is enabled when E=0
Circuit is disabled when E=1
When circuit is disabled, none of the outputs are equal to 0 and none of the minterms are selected
At any given time, only one output is equal to 0, other outputs are 1
2-to-4 Line Decoder with enable input
0

## Slide 41
A decoder can operate with complemented or uncomplemented output
Enable input may be activated with a 0 or a 1 signal
Some decoders may have two or more enable inputs
Block diagram of the 2-to-4 line decoder -
Decoder

## Slide 42
A decoder produces 2n minterms of n-inputs
Any boolean function can be expressed in sum of minterms form
So, a decoder can be used to generate minterms, and an external OR gate to form the sum
Any combinational circuit can be implemented with a decoder and OR gates
Implementing a combinational circuit with a decoder and OR gates requires the boolean function of the circuit be expressed in sum of minterms
COMBINATIONAL LOGIC IMPLEMENTATION

## Slide 43
From the table of the full-adder, function for this circuit in sum of minterms:
  S = X’Y’Z + X’YZ’ + XY’Z’ + XYZ or S(x, y, z) = ∑(1, 2, 4, 7)
  C = X’YZ + XY’Z + XYZ’ + XYZ or C(x, y, z) = ∑(3, 5, 6, 7)
Full-adder circuit has 3 inputs and total 8 outputs, we need 3-to-8-line decoder
Decoder generates the 8 minterms for x,y,z
The OR gate for output S forms the sum of minterms 1,2,4 and 7
The OR gate for output C forms the sum of minterms 3,5,6,and 7
IMPLEMENTING FULL ADDER USING DECODER

## Slide 44
Demultiplexer: A demultiplexer is a circuit that receives information from a single line and transmits this information it to one of 2n possible output lines.
The selection of a specific output is controlled by the bit combination of n selection lines.
The decoder can function as 1-to-4-line demultiplexer when E is taken as a data input line and A and B are taken as the selection inputs.
DEMULTIPLEXER

## Slide 45
The single input variable E has a path to all four outputs, but the input information is directed to only one of the output lines, as specified by the binary combination of the two selection lines A and B
Example, if the selection lines AB = 10, output D2 will be the same as the input value E , while all other outputs are maintained at 1.
As decoder and demultiplexer operations are obtained from the same circuit, a decoder with an enable input is referred to as a decoder – demultiplexer
DEMULTIPLEXER

## Slide 46
Decoder/ Demultiplexer can be connected together to form a larger decoder circuit
Example, two 3-to-8-line decoders with enable inputs connected to form a 4-to-16-line decoder
When w = 0, the top decoder is enabled and the other is disabled.
The bottom decoder outputs are all 0’s, and the top eight outputs generate minterms 0000 to 0111.
When w = 1, the enable conditions are reversed: The bottom decoder outputs generate minterms 1000 to 1111, while the outputs of the top decoder are all 0’s.
DECODER EXPANSION

## Slide 47: ENCODER
Does reverse operation to decoder
An encoder has 2n (or fewer) input lines and n output lines
Constraint – only one input is active at a time
An encoder is a digital circuit that has 2n or fewer input lines and n output lines. The output lines generate the binary code corresponding to the input value
Example – Octal to binary encoder
      Has 8 inputs, one for each octal digit
      3 outputs, that generates the corresponding binary number
      It is assumed that, only one input has a value of 1 at a given time

## Slide 48: ENCODER
D7 D6 D5 D4 D3 D2 D1D0 | X Y Z
0 0 0 0 0 0 0 1 | 0 0 0
0 0 0 0 0 0 1 0 | 0 0 1
0 0 0 0 0 1 0 0 | 0 1 0
0 0 0 0 1 0 0 0 | 0 1 1
0 0 0 1 0 0 0 0 | 1 0 0
0 0 1 0 0 0 0 0 | 1 0 1
0 1 0 0 0 0 0 0 | 1 1 0
1 0 0 0 0 0 0 0 | 1 1 1
Octal to Binary encoder truth table
Binary Encoder
X
Y
Z
D7
D6 D5
D4 D3
D2
D1
D0

## Slide 49: ENCODER
Limitations of the previous encoder –
    Only one input can be active at any given time: If two inputs are active simultaneously, output produces undefined combination. I.e. If D3 and D6 are active at the same time, output of the encoder will be 111 which is neither binary 3 nor binary 6. To solve this limitation, priority encoder is introduced.
    When all the inputs are 0, output of the encoder will be 000. Again, output of the encoder will be 000 if D0 is equal to 1. This can be resolved by providing an additional output indicating that none of the inputs are active.

## Slide 50: PRIORITY ENCODER
A priority encoder is a special type of encoder circuit that includes priority function
Multiple inputs maybe active at the same time
Highest priority input gets the precedence
D3 has the highest priority, then D2 has the
second highest priority and so on.
When input D3 is equal to 1, regardless of the
values of the other inputs, output for XY will be 11(binary 3)
As D2 has the second highest priority level, when D2 = 1, regardless of the values of the other two lower priority inputs(D1 and D0), the output for XY will be 10, given that D3 must be equal to 0
A Valid-output indicator, set to 1 when one or more of the inputs are active
When all inputs are inactive, V=0, other two outputs of the circuit are not used

## Slide 51: PRIORITY ENCODER
Priority Encoder
V
Y
X
D3
D2
D1
D0

## Slide 52: PRIORITY ENCODER

## Slide 53: MULTIPLEXER
A digital multiplexer is a combinational circuit that selects binary information from one of many input lines and directs it to a single output line
There are n selection lines whose bit combinations determine which input is selected.
Generally there are 2n input lines, n selection lines
Each of the two input lines I0 and I1
applied to one input of an AND gate
Selection line S decoded to select a
particular AND gate
2 to 1 line multiplexer

## Slide 54: 4 to 1 LINE MULTIPLEXER
In this circuit, there are 4 input lines, 2 selection lines
Each of the four input lines I0 to I3 applied to one input of an AND gate
Selection lines S1 and S0 decoded to select a
particular AND gate
4 to 1 line multiplexer
Block diagram of a 4 to 1 line multiplexer
Function table of a 4 to 1 line multiplexer

## Slide 55: 4 to 1 LINE MULTIPLEXER
When S1S0=10, AND gate associated with I2 has two of its input equal to 1 and the third input is connected to I2.
Other 3 AND gates has atleast one input equal to 0,
making their output equal to 0
The OR gate output is now equal to the value of I2
4 to 1 line multiplexer
Block diagram of a 4 to 1 line multiplexer
Function table of a 4 to 1 line multiplexer

## Slide 56: FUNCTION IMPLEMENTATION USING MUX
Any boolean function can be implemented by using a multiplexer
A boolean function of n+1 variables can be implemented by taking n variables to the selection lines of the multiplexer.
The remaining variable is used as the input line for the multiplexer
Example- F(A, B, C) = ∑(1, 3, 5, 6)
Steps:
Choose the selector variables. Lets choose,
  B, C as selector S1 and S0
  A as input line

## Slide 57: FUNCTION IMPLEMENTATION USING MUX
Example- F(A, B, C) = ∑(1, 3, 5, 6)
Steps:
In the first row, list the name of the input lines of the multiplexers horizontally
In the second row, list the minterms where A is complemented
In the third row, list the minterms where A is uncomplemented
Circle the minterms for which the function outputs 1
Fourth row presents the multiplexer inputs
  If the two minterms in a column are not circled, apply 0 to the corresponding multiplexer input
  If the two minterms in a column are circled, apply 1 to the corresponding multiplexer input
  If the bottom minterm is circled and the top is not circled, apply A to the corresponding multiplexer input
  If the top minterm is circled and the bottom is not circled, apply A’ to the corresponding multiplexer input

## Slide 58: FUNCTION IMPLEMENTATION USING MUX
MUX input line | I0 | I1 | I2 | I3
A’ | 0 | 1 | 2 | 3
A | 4 | 5 | 6 | 7
Input values | 0 | 1 | A | A’
F(A, B, C) = ∑(1, 3, 5, 6)
4x1 MUX
A B C
S1 S0
I0
I1
I2
I3
0
1

## Slide 59: FUNCTION IMPLEMENTATION USING MUX
MUX input line | I0 | I1 | I2 | I3
A’ | 0 | 1 | 2 | 3
A | 4 | 5 | 6 | 7
Input values | A | 1 | A’ | 0
F(A, B, C) = ∑(1, 2, 4, 5)
4x1 MUX
A B C
S1 S0
I0
I1
I2
I3
1
0

## Slide 60: FUNCTION IMPLEMENTATION USING MUX
It is not necessary to choose the leftmost variable in the ordered sequence of a variable list for the data inputs of the multiplexer. Any of the variable can be chosen to be the input
F(A, B, C) = ∑(1, 2, 4, 5)
MUX input line | I0 | I1 | I2 | I3
Z’ | 0 | 2 | 4 | 6
Z | 1 | 3 | 5 | 7
Input values | Z | Z’ | 1 | 0
4x1 MUX
X Y
S1 S0
I0
I1
I2
I3
0
1
Z

## Slide 61: Self Study
Why is a multiplexer called data selector?
Logic diagram of a quadruple 2 to 1 line multiplexer.(177PAGE)
Exercises from chapter 5:
          5-17,5-18,5-20,5-23,5-24(book slide 208)
Implement the following function with a multiplexer
F(A, B, C,D) = ∑(0,1, 3, 4, 8,9,15)