## Slide 1: CSE 201: Digital Logic Design
Prepared By
Lec Sumaiya Afroz Mila
CSE, MIST

## Slide 2: SEQUENTIAL CIRCUIT
Consist of a combinational circuit to which storage elements are connected to form a feedback path
The storage elements are devices capable of storing binary information.
State of a circuit: Binary information stored in these elements at any given time
The state of the memory devices now, also called current state
Next states and outputs are functions of inputs and present states of storage elements
Memory elements examples- latch, flip-flop

## Slide 3: LATCH
Can store binary information(0 or 1) indefinitely (as long as power is provided)
Building block or basic circuit of other memory elements
Level-triggered memory element
Constructed with NOR gates or NAND gates

## Slide 4: SR LATCH
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Truth Table of NOR gate
S | R | Q | Q’
1 | 0 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 0 | 0 | 1
1 | 1 | Forbidden | 
Memory
Memory

## Slide 5: SR LATCH
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth Table of NAND gate
S | R | Q | Q’
1 | 0 | 0 | 1
1 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 1 | 1 | 0
0 | 0 | Forbidden | 
Memory
Memory

## Slide 6: TWO TYPES OF SEQUENTIAL CIRCUIT
Asynchronous sequential circuit
  Depends upon the input signals at any instant of time and their change order
  Hard to design
  Works faster as there is no clock
  Status of the memory element is affected any time as soon as the input is changed
  Example - Latch
Synchronous sequential circuit
  Defined from the knowledge of its signals at discrete instants of time
  Much easier to design
  Works slower
  Status of the memory element is affected only at the active edge of clock if input is changed
  Example – flip flop

## Slide 7: SYNCHRONOUS CLOCKED SEQUENTIAL CIRCUIT

## Slide 8: MEMORY ELEMENTS
Latch - a level-sensitive memory element
    Examples -
        SR latches
        D latches
Flip-Flop - an edge-triggered memory element
  Examples-
        Master-slave flip-flop
        Edge-triggered flip-flop
RAM and ROM  a mass memory element
C
CLK
Positive Edge
CLK
Negative Edge

## Slide 9: SR FLIP-FLOP

## Slide 10: SR FLIP FLOP
S | R | Q | Q’
1 | 0 | 0 | 1
1 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 1 | 1 | 0
0 | 0 | Invalid | 
Memory
Memory
S | R | Q | Q’
0 | 0 | Invalid | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory | 

## Slide 11: SR FLIP FLOP
S* | R* | Q | Q’
0 | 0 | Invalid | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory | 
S*
R*
Graphic symbol of SR flip flop
CP | S | R | Q | Q’
0 | x | x | Memory | 
1 | 0 | 0 | Memory | 
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | Invalid | 
S* = (S . CP) ‘
= S’ + CP’
R* = (R . CP) ‘
= R’ + CP’

## Slide 12: SR FLIP FLOP
Qt | S | R | Qt+1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | invalid
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | invalid
CP | S | R | Qt+1
0 | x | x | Qt
1 | 0 | 0 | Qt
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Invalid
Truth Table of SR flip flop
Characteristics Table of SR flip flop
Excitation Table of SR flip flop
Qt | Qt+1 | S | R
0 | 0 | 0 | X
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | 0

## Slide 13: SR FLIP FLOP
Qt | S | R | Qt+1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | invalid
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | invalid
Characteristics Table of SR flip flop
Characteristics Equation of SR flip flop
0 | 0 | X | 1
1 | 0 | X | 1
00
01
11
10
0
1
Qt
SR
Qt+1 = S + QtR’
What is the value of Q’t+1?

## Slide 14: SR FLIP FLOP
Excitation Table of SR flip flop
Qt | Qt+1 | S | R
0 | 0 | 0 | X
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | 0
Similarly find the value of S and R

## Slide 15: D FLIP-FLOP

## Slide 16: SR LATCH with NAND GATE
S | R | Q | Q’
1 | 0 | 0 | 1
1 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 1 | 1 | 0
0 | 0 | Invalid | 
Memory
Memory
S | R | Q | Q’
0 | 0 | Invalid | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory | 

## Slide 17: LIMITATIONS in SR FLIP FLOP
S*
R*
S* | R* | Q | Q’
0 | 0 | Invalid | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory | 
It has an invalid input combination. Circuit gives unexpected outcome if such combination occurs. In D flip-flop this combination is eliminated.
CP | S | R | Q | Q’
0 | x | x | Memory | 
1 | 0 | 0 | Memory | 
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | Invalid | 

## Slide 18: D (DATA) FLIP FLOP
CLK | D | Qt+1
0 | X | Qt
1 | 0 | 0
1 | 1 | 1
CP | S | R | Qt+1
0 | x | x | Qt
1 | 0 | 0 | Qt
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Invalid
Truth Table of SR flip flop
Truth Table of D flip flop
S*
R*
Graphic symbol of SR flip flop
Same as SR flip flop

## Slide 19: D FLIP FLOP
Qt | D | Qt+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Truth Table of D flip flop
Characteristics Table of D flip flop
Excitation Table of D flip flop
Qt | Qt+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
CLK | D | Qt+1
0 | X | Qt
1 | 0 | 0
1 | 1 | 1

## Slide 20: JK FLIP-FLOP

## Slide 21: SR LATCH with NOR GATE
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Truth Table of NOR gate
S | R | Q | Q’
1 | 0 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 0 | 0 | 1
1 | 1 | Forbidden | 
Memory
Memory

## Slide 22: SR LATCH
S | R | Q | Q’
1 | 0 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 0 | 0 | 1
1 | 1 | Forbidden | 
Memory
Memory
S | R | Q | Q’
0 | 0 | Memory | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | Forbidden | 

## Slide 23: JK FLIP FLOP
S*
R*
Q | J | K | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
R* = Q.K.CP
S* = Q’. J.CP
S* | R* | Q | Q’
0 | 0 | Memory | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | Forbidden | 
Characteristics Table of JK flip flop

## Slide 24: JK FLIP FLOP
Characteristics Table of JK flip flop
Excitation Table of JK flip flop
Qt | Qt+1 | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
Q | J | K | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 25: T FLIP-FLOP

## Slide 26: T FLIP FLOP
S*
R*
Q | T | Q(t+1)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
S* = Q’.T.CP
R* = Q. T.CP
S* | R* | Q | Q’
0 | 0 | Memory | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | Forbidden | 
Characteristics Table of JK flip flop
Excitation Table of D flip flop
Qt | Qt+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 27: Analysis of Sequential Circuit

## Slide 28: Analysis of Clocked Sequential Circuits: Terminology
STATE EQUATION : A state equation is an algebraic expression that specifies the conditions for a flip-flop state transition.
Left side of the equation denotes the next state and right side is a boolean function that specifies the present state conditions that make the next state equal to 1.
STATE TABLE : A state table consists of 3 sections – Present state, Next state and output(if there is any). [We will need the characteristics table to form state table]
STATE DIAGRAM: The information in a state table can be represented graphically in a state diagram.
The state is represented by a circle and the transitions between states are indicated by directed lines connecting the circles.

## Slide 29: Characteristics Tables

## Slide 30: Steps for Analyzing Clocked Sequential Circuits
At first, find out the flip-flop specified in the question
Derive the input equation of the circuit
Generate the state table with the help of input equation and characteristics table of that flip-flop
Derive the state equation from the state table
Draw the state diagram from the state table

## Slide 31: Analysis of Clocked Sequential Circuits: Example 1
You are given a circuit. Analyse it.

## Slide 32: Analysis of Clocked Sequential Circuits: Example 1
Input Equation:
DA = A(t)x(t) + B(t)x(t)
DB = A’(t)x(t)
Y = [A+B] x’
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | DA | DB | y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0 | 0
State Table

## Slide 33: Analysis of Clocked Sequential Circuits: Example 1 Cntd.
Input Equation:
DA = A(t)x(t) + B(t)x(t)
DB = A’(t)x(t)
Y = [A+B] x’
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | DA | DB | y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0 | 0
State Table
State Equation
0 | 0 | 1 | 0
0 | 1 | 1 | 0
A(t+1):
A
BX
00
01
11
10
0
1
A(t+1): Bx + Ax
B(t+1):
0 | 1 | 1 | 0
0 | 0 | 0 | 0
A
BX
00
01
11
10
0
1
B(t+1): A’x

## Slide 34: Analysis of Clocked Sequential Circuits: Example 1 Cntd.
Input Equation:
DA = A(t)x(t) + B(t)x(t)
DB = A’(t)x(t)
Y = [A+B] x’
State Diagram
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | DA | DB | y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0 | 0
State Table

## Slide 35: Analysis of Clocked Sequential Circuits: Example 2
Input Equation:
You are given input equations of a circuit. Analyse it.

## Slide 36: Analysis of Clocked Sequential Circuits: Example 2 Cntd.
Input Equation:

## Slide 37: Analysis of Clocked Sequential Circuits: Example 2 Cntd.
Present State |  | Input | Next State |  | Flip Flop Inputs |  |  | 
A | B | x | At+1 | Bt+1 | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
State Table
Input Equation:
0 | 0 | 1 | 1
1 | 1 | 1 | 0
A(t+1):
A
BX
00
01
11
10
0
1
A(t+1): A’B + Ax + AB’
1 | 0 | 0 | 1
1 | 0 | 1 | 0
B(t+1):
A
BX
00
01
11
10
0
1
B(t+1): B’x’ + A’x’ + ABx

## Slide 38: Analysis of Clocked Sequential Circuits: Example 2 Cntd.
Present State |  | Input | Next State |  | Flip Flop Inputs |  |  | 
A | B | x | At+1 | Bt+1 | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
State Table
Input Equation:

## Slide 39: Analysis of Clocked Sequential Circuits: Example 3
Present State | Input |  | Next State | Flip Flop Inputs
A | x | y | At+1 | DA
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
State Table
Input Equation:

## Slide 40: Analysis of Clocked Sequential Circuits: Example 3 Cntd.
Present State | Input |  | Next State | Flip Flop Inputs
A | x | y | At+1 | DA
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
State Table
Input Equation:
0 | 1 | 0 | 1
1 | 0 | 1 | 0
XY
00
01
11
10
0
A(t+1): A’x’y + A’xy’+Ax’y’+ Axy
= A’ (x’y+xy’) + A (x’y’+xy)
= A’ (x xor y) + A (x xnor y)
= A xor x xor y
A
1

## Slide 41: Analysis of Clocked Sequential Circuits: Example 4(self study)
Input Equation:
Try analyzing a circuit containing the above input equation
ANSWER
A(t+1)=A’Bx+AB’+Ax’
B(t+1)=B’x+Bx’

## Slide 42: State Reduction & Assignment

## Slide 43
State reduction is required to minimize the cost of the final circuit
State reduction algorithms are concerned with procedures for reducing the number of states in a state table without affecting the input-output sequence
Two circuits are said to be equivalent:
      If identical outputs occur for all input sequences
      Number of states is not important
An algorithm for state reduction:
  Two states are said to be equivalent
    For each member of the set of inputs, they give exactly the same output and send the circuit to the same state or to an equivalent state.
  One of them can be removed without altering the input output relations
State Reduction

## Slide 44
Total states : 7
Consider an Input sequence: 0 1 0 1 0 1 1 0 1 0 0, starting with a, The complete sequence will be:
If we can find a circuit whose state diagram has less than 7 states, and identical outputs occur for the above input sequence and all other possible sequences, then the two circuits are said to be equivalent
State Reduction Example 1

## Slide 45
We will apply the algorithm to this state table
Look for two present states that go to the same next state and have the same output for both input combinations
  1. e = g (remove g);
  2. Replace all g by e
State Reduction Example 1

## Slide 46
  d = f (remove f);
State Reduction Example 1

## Slide 47
  Reduced state table
State Reduction Example 1
New output and state sequence for the previous input sequence: 0 1 0 1 0 1 1 0 1 0 0

## Slide 48
Previous state Sequence
  New state Sequence
State Reduction Example 1

## Slide 49
Reduced state Diagram
State Reduction Example 1

## Slide 50
State Reduction Example 2
Present State | Next State |  | Output | 
 | X=0 | X=1 | X=0 | X=1
A | F | B | 0 | 0
B | D | C | 0 | 0
C | F | E | 0 | 0
D | G | A | 1 | 0
E | D | C | 0 | 0
F | F | B | 1 | 1
G | G | D | 0 | 1

## Slide 51: State Assignment
Assign coded binary values to the states for physical implementation
For a circuit with m states, the codes must contain n bits where 2n >= m
Unused states are treated as don’t care conditions during the design
  Don’t cares can help to obtain a simpler circuit
There are many possible state assignments
  Have large impacts on the final circuit size

## Slide 52: Popular State Assignment

## Slide 53: State Assignment
Any binary number assignment is satisfactory as long as each state is assigned a unique number
Use binary assignment 1

## Slide 54: Mealy and Moore Model

## Slide 55: Mealy and Moore Model
All the sequential circuits have input, output and internal states
Sequential circuits can be divided into two types based on their characteristics:
    Mealy Model of sequential circuits
        &
    Moore Model of sequential circuits
They differ only in the way their output is generated
    Mealy Model: The output is a function of both the present state and the input
    Moore Model: The output is a function of only the present state

## Slide 56: Block Diagram of Mealy and Moore Machine

## Slide 57: Example of Mealy Machine
This circuit is an example of Mealy Machine
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | DA | DB | y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0 | 0

## Slide 58: Example of Mealy Machine
The output y is a function of both present state AB and input x.
For present state 01
    when input x=0; output is 1
    when input x=1; output is 0
For the same state, the output changes with the input
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | DA | DB | y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0 | 0

## Slide 59: Example of Moore Machine
This circuit is an example of Moore Machine
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | TA | TB | y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1

## Slide 60: Example of Mealy Machine
The output y is a function of only present state AB
For present state 01
    when input x=0; output is 0
    when input x=1; output is 0
This is same for all the combinations
For the same state, the output does not change with the input
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | TA | TB | y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1

## Slide 61: Design of Sequential Circuit

## Slide 62: Steps of Design Procedure
Derive a state diagram for the circuit
Reduce the number of states if necessary
Assign binary values to the states
Obtain the binary coded state table
Choose the type of flip flop to be used
Derive the simplified flip flop input equation and output equation
Draw the logic diagram

## Slide 63: Excitation Tables

## Slide 64: Example 1: State Diagram For Design
Present State |  | Input | Next State | 
A | B | x | At+1 | Bt+1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
State Table for Circuit Design

## Slide 65: Example 1: State Diagram For Design
Let’s design the circuit with JK flip flop first
Present State |  | Input | Next State |  | Flip Flop Inputs |  |  | 
A | B | x | At+1 | Bt+1 | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 | 0 | X | 0 | X
0 | 0 | 1 | 0 | 1 | 0 | X | 1 | X
0 | 1 | 0 | 1 | 0 | 1 | X | X | 1
0 | 1 | 1 | 0 | 1 | 0 | X | X | 0
1 | 0 | 0 | 1 | 0 | X | 0 | 0 | X
1 | 0 | 1 | 1 | 1 | X | 0 | 1 | X
1 | 1 | 0 | 1 | 1 | X | 0 | X | 0
1 | 1 | 1 | 0 | 0 | X | 1 | X | 1

## Slide 66: Example 1: State Diagram For Design
Present State |  | Input | Next State |  | Flip Flop Inputs |  |  | 
A | B | x | At+1 | Bt+1 | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 | 0 | X | 0 | X
0 | 0 | 1 | 0 | 1 | 0 | X | 1 | X
0 | 1 | 0 | 1 | 0 | 1 | X | X | 1
0 | 1 | 1 | 0 | 1 | 0 | X | X | 0
1 | 0 | 0 | 1 | 0 | X | 0 | 0 | X
1 | 0 | 1 | 1 | 1 | X | 0 | 1 | X
1 | 1 | 0 | 1 | 1 | X | 0 | X | 0
1 | 1 | 1 | 0 | 0 | X | 1 | X | 1

## Slide 67: Example 1: State Diagram For Design

## Slide 68: Example 2: State Diagram For Design
Present State |  | Input | Next State | 
A | B | x | At+1 | Bt+1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
State Table for Circuit Design

## Slide 69: Example: 2 State Diagram For Design
Let’s design the circuit with D flip flop first
Present State |  | Input | Next State |  | Flip Flop Inputs | 
A | B | x | At+1 | Bt+1 | DA | DB
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 70: Example 2: State Diagram For Design
Present State |  | Input | Next State |  | Flip Flop Inputs | 
A | B | x | At+1 | Bt+1 | DA | DB
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 71: Example 2: State Diagram For Design

## Slide 72: Example 3: State Diagram For Design
0/0
1/1
1/0
0/0
0/0
1/1
0/0
1/0
Present State |  | Input | Next State |  | Output
A | B | x | At+1 | Bt+1 | Y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0

## Slide 73: Example 3: State Diagram For Design
Let’s design the circuit with D flip flop first
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | DA | DB | Y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0

## Slide 74: Example 3: State Diagram For Design
Present State |  | Input | Next State |  | Flip Flop Inputs |  | Output
A | B | x | At+1 | Bt+1 | DA | DB | Y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0

## Slide 75: Example 3: State Diagram For Design

## Slide 76: Design of Counters

## Slide 77: Counters
An n-bit binary counter consists of n flip-flops
Can count in binary from 0 to 2n-1
Here is a state diagram of 3-bit binary counter
Next state of the counter depends entirely on its present state
State transition occurs every time a pulse occurs

## Slide 78: Example 1: Design of Counters
Design the counter with the following state diagram with T flip-flop/
Design a 3-bit binary counter with T flip flop

## Slide 79: Example 1: Design of Counters
Design the counter with T flip-flop

## Slide 80: Example 1: Design of Counters

## Slide 81: Example 1: Design of Counters

## Slide 82: Example 2: Design of Counters
Design the counter with the following state diagram with JK flip-flop/
Design a 3-bit binary counter with JK flip-flop

## Slide 83: Example 2: Design of Counters
Present State |  |  | Next State |  |  | Flip Flop Inputs |  |  |  |  | 
A | B | C | A | B | C | JA | KA | JB | KB | JC | KC
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | X | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | X | 1 | X | 1
1 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0 | X | 1 | X
1 | 0 | 1 | 1 | 1 | 0 | X | 0 | 1 | X | X | 1
1 | 1 | 0 | 1 | 1 | 1 | X | 0 | X | 0 | 1 | X
1 | 1 | 1 | 0 | 0 | 0 | X | 1 | X | 1 | X | 1

## Slide 84: Example 2: Design of Counters
Present State |  |  | Next State |  |  | Flip Flop Inputs |  |  |  |  | 
A | B | C | A | B | C | JA | KA | JB | KB | JC | KC
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | X | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | X | 1 | X | 1
1 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0 | X | 1 | X
1 | 0 | 1 | 1 | 1 | 0 | X | 0 | 1 | X | X | 1
1 | 1 | 0 | 1 | 1 | 1 | X | 0 | X | 0 | 1 | X
1 | 1 | 1 | 0 | 0 | 0 | X | 1 | X | 1 | X | 1
 |  | 1 | 
X | X | X | X
A2
A1A0
00
01
10
11
JA = A1A0
X | X | X | X
 |  | 1 | 
A2
00
01
10
11
KA = A1A0
A1A0

## Slide 85: Example 2: Design of Counters
Present State |  |  | Next State |  |  | Flip Flop Inputs |  |  |  |  | 
A | B | C | A | B | C | JA | KA | JB | KB | JC | KC
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | X | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | X | 1 | X | 1
1 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0 | X | 1 | X
1 | 0 | 1 | 1 | 1 | 0 | X | 0 | 1 | X | X | 1
1 | 1 | 0 | 1 | 1 | 1 | X | 0 | X | 0 | 1 | X
1 | 1 | 1 | 0 | 0 | 0 | X | 1 | X | 1 | X | 1
 | 1 | X | X
 | 1 | X | X
A2
A1A0
00
01
10
11
JB= A0
X | X | 1 | 
 | 1 | X | X
A2
00
01
10
11
KB = A0
A1A0

## Slide 86: Example 2: Design of Counters
Present State |  |  | Next State |  |  | Flip Flop Inputs |  |  |  |  | 
A | B | C | A | B | C | JA | KA | JB | KB | JC | KC
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | X | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | X | 1 | X | 1
1 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0 | X | 1 | X
1 | 0 | 1 | 1 | 1 | 0 | X | 0 | 1 | X | X | 1
1 | 1 | 0 | 1 | 1 | 1 | X | 0 | X | 0 | 1 | X
1 | 1 | 1 | 0 | 0 | 0 | X | 1 | X | 1 | X | 1
1 | X | X | 1
1 | X | X | 1
A2
A1A0
00
01
10
11
JC= 1
X | 1 | 1 | X
X | 1 | 1 | X
A2
00
01
10
11
KC = 1
A1A0

## Slide 87: Example 2: Design of Counters
Functions for 3-bit binary counter with JK flip flop
JA = A1A0
KA = A1A0
JB= A0
KB = A0
JC= 1
KC = 1

## Slide 88: Self Study
Exercises from chapter 6:
          6-14,6-15,6-16