## Slide 1: Pulse Transformer
Muhaimin Bin Munir

## Slide 2: Application of Pulse Transformer
To change the amplitude and impedance level of a pulse
To invert the polarity of a pulse; also to provide with the aid of center-tapped winding, equal positive and negative pulses simultaneously.
To produce a pulse in a circuit having negligible d-c resistance
To effect “d-c isolation” between source and a load; in other words, to produce a pulse in a winding whose d-c voltage level may be arbitrarily selected
To couple between stages of pulse amplifiers
To differentiate a pulse
To act as a coupling element in certain pulse-generating circuits such as the blocking oscillator and multiar

## Slide 3: Advantages
Passive circuit element
Stable
No additional voltage required for operation
Separates High voltage power circuit from Low voltage power circuit
Small in size (High frequency)
Multiple components in secondary

## Slide 4: Transformer
Fig: Diagram of a Transformer
Fig: Schematic Diagram of a Transformer

## Slide 5: Coefficient of Coupling
LP = Primary Inductance LS = Secondary Inductance M = Mutual Inductance RL = Load Resistance K = Coefficient of Coupling K = M/√(LPLS)
Things we ignored
Primary Resistance
Secondary Resistance
Source Resistance
Capacitance
Core Loss
Non-linear behaviour of magnetic ckt

## Slide 6: η = vo/vi = iP /iS = √(LP/LS) = NS/NP

## Slide 8: Equivalent Circuit...
1/α = Transformation Ratio α = constant iS/α = Load current reflected into primary α2RL= Load Resistance reflected into primary Still Unknown σ2 = ? σ1 = ? L = ?

## Slide 9: Equivalent Circuit...
V1 = (R1+R2)i1 - R2i2 0 = (R2+R3)i2 - R2i1
vi = LPdip/dt - Mdis/dt 0 = -Mdip/dt + Lsdis/dt + isRL
vi = (σ1 + L)dip/dt - L d/dt(is/α) 0 = -Ldip/dt +(σ2 + L) d/dt(is/α) + α2RL(is/α) = -L/α dip/dt +(σ2 + L)/α2 d/dt(is) + RL(is)

## Slide 10: Equivalent Circuit...
L = αM σ2 = α2Ls- αM σ1 = LP- αM
Case: 1
α = √(LP /Ls)
σ1 = LP(1-K) σ2 = LP(1-K) L = KLP

## Slide 11: Equivalent Circuit...
L = αM σ2 = α2Ls- αM σ1 = LP- αM
Case: 2
α = 1/K √(LP /Ls)
σ1 = 0 σ2 = LP(1/K2 - 1) L = LP

## Slide 12: Equivalent Circuit...
L = αM σ2 = α2Ls- αM σ1 = LP- αM
Case: 3
α = K √(LP /Ls)
σ1 = LP(1 - K2) σ2 = 0 L = K2LP

## Slide 13: Output of Pulse Transformer
L/Ro > 10T [High Frequency]
L/Ro < T/10 [Low Frequency]

## Slide 14: Fortune and misfortune are like twisted ropes, so they come by turns. -Captain Ri Jeong Hyeok