## Slide 1: Case 1: A=0 & E=1
For corresponding input of E diode D1 & diode D4 are "Reverse Biased" (open circuited)
For input A diode D2 work as "Forward Biased" (short circuited)
Now if we consider the point between D2 & D3 as VB1, we see that on VB1 point the available voltage is (0.7+0.2) 0.9 V
If we want to bias D3 diode as forward mode ,then the required voltage on VB1 point is VB1(req)=D3+VBE2+VBE3 (0.65+0.65+0.65) is 1.95V
As we see that on VB1 point the required voltage greater than existing voltage D3 diode work as "Reverse Bias"
Because of low voltage T2 is therefore on "OFF" state and so T3 is also on "OFF" state. So T3 is not connected to Vo
From Vcc T4 get high input voltage. So T4 is on "ON" state.
Diode D also get high input. So D is also on "Forward Bias"
Hence Vout get connected to Vcc. So we get high or 1 on Vout

## Slide 2: Case 2: A=1 & E=1
For corresponding input of A & E diode D1, diode D4, diode D2 are on "Reverse " Bias
Because of Vcc voltage diode D3 get high input . So D3 is at "Reverse" Bias
Then base of T2 transistor get high input. So T2 transistor is at "ON" state
From T2 current will flow on RE1. This current and resistance create sufficient voltage to turn on the T3 transistor. So T3 is at "ON" state or short circuited
If we consider the point between of RC1 resistance and T4 transistor as VB2 , we see that the available voltage on VB2 point (VCE(sat)+VBE=0.2+0.7) 0.9 V
If we want to ON t4 transistor the required voltage on VB2 point is VB2=VBE4+VD (0.65+0.65) is 1.3 V
As we see that on VB2 point the required voltage greater than existing voltage. So, Transistor T4 work as "Reverse" bias.
Then diode D also don't get sufficient voltage to "ON". So diode D is at "Reverse" bias.
So the path between Vcc and Vo is open and Vo connected to ground through short circuit. Hence we get low or 1 on Vo

## Slide 3: Case 3 &4: A=0/1 & E=0
For corresponding input of E diode D1 & D4 are " Forward " Biased.(short circuit)
If we consider the junction of diode D2 & diode D3 as VB1. Then as VB1 point connected to input E through short circuit. Vb1 point always get low voltage.
Now if we put 0 on input A then diode D2 is at "ON" state. If we put 1 on input A then diode D2 is at "OFF" state. On both case the point VB1 geet low voltage
If put A=0 then D2 is at "Forward" bias. On VB1 point the available voltage is (0.7+0.2) 0.9 V. If we put A=1 then the voltage at that point is more less than that.
If we want to bias D3 diode as forward mode ,then the required voltage on VB1 point is VB1(req)=D3+VBE2+VBE3 (0.65+0.65+0.65) is 1.95V
So we see that whatever input we put on A ,VB1 point can't make the diode D3 on "forward " mode.
As D3 is "Reverse" biased ,T2 transistor also get low voltage and so T3 get low voltage. So T2 & T3 is at "OFF" state.
In figure we see that T4 transistor connected to input E which is on low voltage. So T4 transistor also get low voltage that means it's on " Reverse" bias.
For that reason diode D also on "Reverse" bias.
As transistor T3 and transistor T4 both are on "OFF" state ,the output Vo is on "Floating" state.
This state os output is called High Impedance state.