## Slide 1: Introduction to 8086 Microprocessor

## Slide 3: 8086 Pin Diagram

## Slide 4: Pin Description
AD0-AD15: Multiplexed Address/Data Bus
RD’: Low while reading from memory or port
WR’ : Low while writing to memory or port
ALE : Address latch enable shows 8086 data bus contains address information. This address can be a memory or I/O device
M/IO’ : High during Memory operations.
Low during I/O Port operations.
RESET: causes the processor to immediately terminate its present activity. The signal must be active HIGH for at least four clock cycles. It restarts execution.

## Slide 5: Pin Description
CLK : The clock pin provides the basic timing signal to the microprocessor
VCC: This power supply input provides a +5.0 V ±10 % signal to the microprocessor.
GND: The ground connection is the return for the power supply. Note that the 8086 microprocessors have two pins labeled GND—both must be connected to ground for proper operation.

## Slide 6: Pin Description
INTR-Interrupt Request : Interrupt requests used to request a hardware interrupt.
INTA-Interrupt Acknowledgement : It becomes active after the current instruction has completed execution.
NMI : The non-maskable interrupt is similar to INTR except that the NMI interrupt does not check to see whether the IF flag bit is a logic 1.

## Slide 7: Pin Description
HOLD : The hold input requests a direct memory access (DMA). If the HOLD signal is a logic 1, the microprocessor release the buses for external use. If the HOLD pin is a logic 0, the microprocessor executes software normally.
HLDA : Hold acknowledge indicates that the 8086 has entered the hold state
MN/MX’ In Minimum mode, the 8086 processor works in a single processor environment. Maximum mode is designed to be used when a co-processor exists in the system.
If minimum mode is selected, the MN/MN’ pin must be connected directly to +5.0 V.

## Slide 8: Pin Description
DT/R’ : The data transmit/receive signal shows that the microprocessor data bus is transmitting (DT/R’ ) or receiving (DT/ R’) data. This signal is used to enable external data bus buffers.
BHE’/S7: The bus high enable pin is 0 used to enable the most-significant data bus bits (D15–D8) and 1 to enable data bus bits (D7–D0) during a read or a write operation. The state of S7 is always a logic 1.
READY: The READY input is controlled to insert wait states into the timing of the microprocessor. If the READY pin is placed at a logic 0 level, the micro-processor enters into wait states and remains idle. If the READY pin is placed at a logic 1 level, it has no effect on the operation of the microprocessor.
TEST’: TEST pin is examined by the "WAIT" instruction. If the TEST pin is Low, execution continues. Otherwise the processor waits in an "idle" state.

## Slide 9: Pin Description
A19/S6–A16/S3 : The address/status bus bits are multiplexed to provide address signals A19–A16 and also status bits S6–S3.
During the first clock period of a bus cycle, the entire 20-bit address is available on these lines. During all other clock cycles for memory and I/O operations, AD15-AD0 contains the 16-bit data, and S3, S4, S5, and S6 become status lines.
After the first clock cycle of an instruction execution, the A17/S4 and A16/S3 pins specify which segment register generates the segment portion of the 8086 address.
S5 reflects the contents of the IF flag. S6 is always held at 0 and indicates that an 8086 is controlling the system bus.

## Slide 10: Pin Description
S3 and S4 lines are decoded as follows:
A17/S4 | A16/S3 | Function
0 | 0 | Extra segment access
0 | 1 | Stack segment access
1 | 0 | Code segment access
1 | 1 | Data segment access

## Slide 11: Reference (1)
The address/data bus on the 8086 is multiplexed (shared) to reduce the number of pins required for the 8086/8088 microprocessor integrated circuit. Unfortunately, this burdens the hardware designer with the task of extracting or demultiplexing information from these multiplexed pins.

## Slide 12: Reference (2): Multiplexer (Data Selector)
Multiplexing means transmitting a large number of information units over a smaller number of channels or lines.
A digital multiplexer is a circuit that selects binary information from one of many input lines and directs it to a single output lines.
The selection of a particular input line is controlled by a set of selection lines.
  Have 2n input lines and n selection lines whose bit combinations determine which input is selected.

## Slide 13: Reference (3): Multiplexer

## Slide 14: Reference (4) : 4-to-1-Line Multiplexer
The combinations of S0 and S1 control each AND gates
Part of the multiplexer resembles a decoder
  Selection lines s1 and s0 are decoded to select a particular AND gate.
To construct a multiplexer:
  Start with an n-to-2n decoder
  Add 2n input lines, one to each AND gate
  The outputs of the AND gates are applied to a single OR gate.

## Slide 15: Reference (5) : 4-to-1-Line Multiplexer
    The function table lists the input-to-output path for each possible bit combination of the selection lines.

## Slide 16: Reference (6): Multiplexer
The size of a multiplexer is specified by the number 2n of its input lines and the single output line.
  It is then implied that it also contains n selection lines.
As in decoders, multiplexer ICs may have an enable input to control the operation of the unit.

## Slide 17: Reference (7)

## Slide 18: BUS Buffering and Latching
The 8086 microprocessor shown with a demultiplexed address bus. This is the
model used to build many 8086-based systems
Reference (8)
ALE =1 then this address lines will go to bus also as
AD0 to Ad15 connect to 373 buffers, addresses will
Go to bus.By disabling DEN pin we disable 245 buffers.So
From 0 to 15 nothing pass as data
When ALE =0 then from AD0 to Ad15 we get DATA.Then DEN
Pin enables and 245 buffers become active so 0-15 send
Data to bus