## Slide 1: Assembly Language
Prepared By
Swapnil Biswas
Department of CSE, MIST

## Slide 2: Registers
Type of fast memory
Department of CSE, MIST
Used to store and transfer data and instructions

## Slide 3: Types of Registers
3 types
Department of CSE, MIST
Data Register
Address Register
Status Register
We will mainly focus on Data Register

## Slide 4: Data Register
Holds data
Department of CSE, MIST
16 bit
4 types:
AX: Accumulator Register
BX: Base Register
CX: Count Register
DX: Data Register

## Slide 5: AX: Accumulator Register
16 bit
Department of CSE, MIST
Upper and lower bytes can be used separately
Special Purpose: Multiplication, Division, Input, Output
AX:
AH
AL

## Slide 6: BX: Base Register
16 bit
Department of CSE, MIST
Upper and lower bytes can be used separately
Special Purpose: General purpose register
BX:
BH
BL

## Slide 7: CX: Count Register
16 bit
Department of CSE, MIST
Upper and lower bytes can be used separately
Special Purpose: Controlling loop
CX:
CH
CL

## Slide 8: DX: Data Register
16 bit
Department of CSE, MIST
Upper and lower bytes can be used separately
Special Purpose: Multiplication, Division, Output
DX:
DH
DL

## Slide 9: Representing Numbers
Binary Numbers
Department of CSE, MIST
Find the base of the following numbers
Must end with b
Example: 10110111b
Hexa Numbers
Must end with h
10110111b
Must start with digit
Legal Number: 2Ah
Illegal Number: DAh
Legal Number: 0DAh
Decimal Numbers
Can end with d
Legal Number: 128d
Legal Number: 128
Binary
1Bh
Hexa
10110111
Decimal
3B
Wrong Format
38
Decimal
EAh
Wrong Format
Correct: 0EAh

## Slide 10: Registers and Data Types
Department of CSE, MIST
Register | 16 bit | 8 bit
Accumulator | AX | AH, AL
Base | BX | BH, BL
Count | CX | CH, CL
Data | DX | DH, DL
Data type | Full form | Number of bits
DB | Define Byte | 8
DW | Define Word | 16
DD | Define Double Word | 32
DQ | Quad Word | 64
List of Registers
List of Data Types

## Slide 11: Declaration of Variables
Department of CSE, MIST
Variable Name
Data type
var1
db
Initial Value
5
Must be initialized with a legal value
Verify the following initializations:
Var1 db 320
Illegal
Var1 db 1001100110101b
Illegal
Var1 db 0000000110101b
Legal

## Slide 12: Naming of Variables
Department of CSE, MIST
Can be combination of
Can not be started with digit and can not be consist of only digits
1Var db 127
Illegal
Letter
123 db 127
Legal
Digit
Special Characters like: @ $ ? _
Case insensitive
Verify the following variable names:
Illegal
? db 127
AbC$? db 127
Legal
@1 db 127
Legal

## Slide 13: Format of Instruction
Department of CSE, MIST
Opcode
Operands
Mov
CX,4
Comments
; We don’t code in C, we code in Assembly

## Slide 14: Commonly Used Opcode
Department of CSE

## Slide 15: MOV
MOV DEST, SRC
Department of CSE, MIST
DEST = Registers, Variables
SRC = Registers, Variables, Values
Number of bits (SRC) = Number of bits (DEST)
Example: MOV CX, 8
Equivalent Task: CX = 8
Equivalent Task: DEST = SRC
SRC and DEST can not be variables at a time
Verify the following instructions:
MOV AH, DL
;Illegal
;Legal
MOV var1, AL
; AH = DL
;Legal if Var1 is DB
; var1 = AL
MOV AX,Var1
;Legal if Var1 is DW
; AX = var1
MOV var1, var2
MOV AL,00000000000011b
;Legal
MOV CL, 100000000000b
MOV BH, 287
MOV var1, 125
;Illegal
;Illegal
;Legal

## Slide 16: XCHG
XCHG ARG1, ARG2
Department of CSE, MIST
ARG1 = Registers, Variables
ARG2 = Registers, Variables
Number of bits (ARG1) = Number of bits (ARG2)
Example: XCHG AL, BH
Equivalent Task: SWAP(AL, BH)
Equivalent Task: SWAP(ARG1, ARG2)
ARG1 and ARG2 can not be variables at a time
Verify the following instructions:
XCHG AH, DL
;Illegal
;Legal
XCHG var1, AL
; SWAP(AH, DL)
;Legal if Var1 is DB
; SWAP(var1, AL)
XCHG AX,30
XCHG var1, var2
;Illegal

## Slide 17: ADD
ADD DEST, SRC
Department of CSE, MIST
DEST = Registers, Variables
SRC = Registers, Variables, Values
Number of bits (SRC) = Number of bits (DEST)
Example: ADD AL, BH
Equivalent Task: AL = AL + BH
Equivalent Task: DEST= DEST + SRC
SRC and DEST can not be variables at a time
Verify the following instructions:
ADD AH, DL
;Illegal
;Legal
ADD var1, AL
; AH=AH+DL
;Legal if Var1 is DB
; var1=var1+AL
ADD AX,Var1
;Legal if Var1 is DW
; AX=AX+var1
ADD var1, var2
ADD var1, 125
;Legal
; var1=var1+125
ADD ch, 125
;Legal
; ch=ch+125
;Illegal
ADD 320, al

## Slide 18: SUB
SUB DEST, SRC
Department of CSE, MIST
DEST = Registers, Variables
SRC = Registers, Variables, Values
Number of bits (SRC) = Number of bits (DEST)
Example: SUB AL, BH
Equivalent Task: AL = AL - BH
Equivalent Task: DEST= DEST - SRC
SRC and DEST can not be variables at a time

## Slide 19: NEG
NEG DEST
Department of CSE, MIST
DEST = Registers, Variables
Example: NEG AL
Equivalent Task: AL = - AL
Equivalent Task: DEST= - DEST

## Slide 20: INC
INC DEST
Department of CSE, MIST
DEST = Registers, Variables
Example: INC AL
Equivalent Task: AL = AL + 1
Equivalent Task: DEST= DEST + 1

## Slide 21: DEC
DEC DEST
Department of CSE, MIST
DEST = Registers, Variables
Example: DEC AL
Equivalent Task: AL = AL - 1
Equivalent Task: DEST= DEST - 1

## Slide 22: Task
Write instructions in Assembly Language for the following task:
Department of CSE, MIST
A = B – 2*A
MOV AL, A
[Consider A and B as db type variables]
ADD AL, AL
SUB AL, B
; AL = A
; AL = 2*A
; AL = 2*A - B
MOV A, AL
; A = 2*A - B
NEG A
; A = B – 2*A

## Slide 23: Single Character Input
Required Instruction: INT 21H
Department of CSE, MIST
Set AH = 1 before calling INT 21H
Input character will be stored at AL after calling INT 21H
Value of AH works as Mode Selector here
MOV AH,1
INT 21H
; Now use the input from AL

## Slide 24: Single Character Output
Required Instruction: INT 21H
Department of CSE, MIST
Set AH = 2 before calling INT 21H
Store the output character at DL before calling INT 21H
Value of AH works as Mode Selector here
MOV AH,2
INT 21H
; Set your required character at DL

## Slide 25: String Output
Required Instruction: INT 21H
Department of CSE, MIST
Set AH = 9 before calling INT 21H
Store the output string with a $ at the end as a DB type variable
Move the variable at DX by LEA before calling INT 21H
MOV AH,9
INT 21H
STRING1 DB ‘HELLO WORLD$’
LEA DX, STRING1

## Slide 26: Point To Remember
Value of AL gets changed after calling INT 21H
Department of CSE, MIST
So, if you have a desired value at AL, store it at other place before calling INT 21H

## Slide 27: Thank You
Question?
Department of CSE