## Slide 1
Status and FLAGS Register (Ch-5)
Flow Control Instructions (Ch-6)
Logic, Shift and Rotate Instructions (7)
Multiplication and Division Instructions (9)

## Slide 2: Processor Status and FLAGS Register

## Slide 3: FLAGS Register
Individual bits control the action or represent the status of the processor
  Control flags (TF, IF, DF)
    Determine how the processor responds to certain situations
  Status flags (CF, PF, AF, ZF, SF, OF)
    Set to represent the result of certain operations
    Used to control conditional jump instructions

## Slide 5: Control Flags
DF - Direction flag [String access direction]
  STD: direction = down
  CLD: direction = up
IF - Interrupt enable
  STI: enable external interrupts
  CLI: disable maskable external interrupts
TF - Trace flag
  Interrupt 1 after executing instruction, if set

## Slide 6: Status Flags
The Carry Flag (CF) CF = 1 if there is a carry out from the msb (most significant bit) on addition, or there is a borrow into the msb on subtraction
  CF = 0 otherwise
  CF is also affected by shift and rotate instructions
The Parity Flag (PF) PF = 1 if the low byte of a result has an even number of one bits (even parity)
  PF = 0 otherwise (odd parity)

## Slide 7: Status Flags
The Auxiliary Carry Flag (AF) AF = 1 if there is a carry out from bit 3 on addition, or there is a borrow into the bit 3 on subtraction
  AF = 0 otherwise
  AF is used in binary-coded decimal (BCD) operations
The Zero Flag (ZF) ZF = 1 for a zero result
  ZF = 0 for a non-zero result

## Slide 8: Status Flags
The Sign Flag (SF) SF = 1 if the msb of a result is 1; it means the result is negative if you are giving a signed interpretation
  SF = 0 if the msb is 0
The Overflow Flag (OF) OF = 1 if signed overflow occurred
  OF = 0 otherwise

## Slide 9: (Signed) Overflow
Can only occur when adding numbers of the same sign (subtracting with different signs)
Detected when carry into MSB is not equal to carry out of MSB
  Easily detected because this implies the result has a different sign than the sign of the operands
Signed Overflow Example
10010110 + 10100011 00111001
Carry in = 0, Carry out = 1 Neg+Neg=Pos Signed overflow occurred OF = 1 (set)
00110110 + 01100011 10011001
Carry in = 1, Carry out = 0 Pos+Pos=Neg Signed overflow occurred OF = 1 (set)

## Slide 10: Unsigned Overflow
The carry flag is used to indicate if an unsigned operation overflowed
The processor only adds or subtracts - it does not care if the data is signed or unsigned!
10010110 + 11110011 10001001
Carry out = 1 Unsigned overflow occurred CF = 1 (set)

## Slide 11: Instructions and Flags
MOV and XCHG - no flags are changed
ADD and SUB - all flags affected
INC and DEC - all except CF
NEG - all flags affected
  CF=0 only if value is 0

## Slide 12: Flow Control Instructions

## Slide 13: Flow Control Instructions
Jump and Loop instructions transfer control to another part of the program.
The transfer can be unconditional or can depend on status flags.

## Slide 14: Flow Control Instructions
Conditional jumps:
  Jxxx destination label;
  Destination label must precede the jump instruction by no more than 126 bytes, or follow it by no more than 127 bytes
Machine Code= Opcode Bytes
7x yy

## Slide 15: Conditional jumps
The CMP instruction:
  CMP destination, source
  CMP ax,bx ; ax=7FFFh, bx=0001h
  ; ax-bx = 7FFFEh
  JG Below; STATUS: ZF=SF=OF=0
  Add bx,cx
  ....
  Below:
  ….

## Slide 16: Signed Vs Unsigned Jumps
;ax=7FFFh, bx= 8000h
CMP ax,bx
JA BELOW ; incorrect in a signed sense

## Slide 17: Signed Jumps

## Slide 18: Signed Jumps

## Slide 19: Unsigned Jumps

## Slide 20: Branching Structures
IF-THEN
IF-THEN-ELSE
CASE
AND conditions
OR conditions

## Slide 21: IF-THEN-ELSE structure
mov ah, 2 ; prepare for display ; if al <= bl cmp al, bl ; al <= bl ? jnbe else_ ; no, display bl ; then ; al <= bl mov dl, al ; move it to dl jmp display
else_: ; bl < al
mov dl, bl
display: int 21h ; display it ; endif
if al <= bl then display the character in al else display the character in bl endif

## Slide 22: The CASE structure
; case ax
cmp ax, 0 ; test ax jl neg ; ax < 0 je zero ; ax = 0 jg pos ; ax > 0
neg: mov bx, -1 jmp endcase
zero: mov bx,0 jmp endcase
pos: mov bx, 1 ; put 1 in bx
endcase:
case
ax < 0 : put -1 in bx = 0 : put 0 in bx > 0 : put 1 in bx
endcase

## Slide 23: Looping Structures
FOR loop
WHILE loop
REPEAT loop
Loop structure:
    Top:
    ;loop body
    Loop Top
CX contains the loop counter

## Slide 24: FOR Loop
a counter-controlled loop to display a row of 80 stars
mov cx,80 ; # of stars mov ah,2 ; disp char fnctn mov dl,'*' ; char to display
jcxz end_
TOP:
int 21h ; display a star loop TOP ; repeat 80 times
end_:

## Slide 25: A Loophole
The FOR loop implemented with the loop instruction always executes at least once
If cx = 0 at the beginning, the loop will execute 65536 times!
To prevent this, use a jcxz before the loop
jcxz SKIP
TOP:
; body of loop . . . loop TOP
SKIP:

## Slide 26: WHILE LOOP
Count the number of characters in an input line
mov dx,0 ;DX counts chars mov ah,1 ;read char int 21h ;read char into al
WHILE_:
cmp al,0Dh ;ASCII CR? je ENDWHILE ;yes, exit inc dx ;not CR, inc count int 21h ;read another char jmp WHILE_ ;loop back
ENDWHILE:
count = 0 read char while char <> carriage_return do
Increment count read char
endwhile

## Slide 27: REPEAT LOOP
repeat
read character
until character is a blank
mov ah,1 ;read char function
REPEAT:
int 21h ;read char into al
;until
cmp al,' ' ;a blank? jne REPEAT ;no, keep reading

## Slide 28: Your turn..
Convert into pseudocode:
cmp ax,bx
jl a0 ; ax<bx
cmp bx,cx
jge c0 ;bx>=cx
mov bx,0 ;bx<cx
jmp end_
c0:
mov cx,0 ; cx=0
jmp end_
a0:
mov ax,0 ;ax=0
end_: ; end of code

## Slide 29: Your turn..
Convert into pseudocode:
if (ax<bx) ax=0
else{
if(bx<cx) bx=0
else cx=0
}

## Slide 30: AND conditions
; read a character
mov ah, 1 ;prepare to read
int 21h ;char in al
; if char >= 'A' and char <= 'Z'
cmp al,'A' ;char >= 'A'? jnge endif ;no, exit cmp al,'Z' ;char <= 'Z'? jnle endif ;no, exit
;then display character
mov dl,al ;get char mov ah,2 ;prep for display int 21h ;display char
endif:
read a character into al if char >= 'A' and char <= 'Z' then
display character
endif

## Slide 31: IF-THEN structure
; if ax < 0 cmp ax, 0 ; ax < 0 ? jnl endif ; no, exit ; then neg ax ; yes, change sign endif:
Example -- to compute |ax|:
if ax < 0 then ax = -ax endif

## Slide 32: Multiplication and Division Instructions

## Slide 33: Multiplication instructions
imul source
  Signed multiply
mul source
  Unsigned multiply
Byte and Word Multiplication (A X B)
  If two bytes are multiplied, the result is a 16-bit word
    A: source
    B: al
    product: ax
  If two words are multiplied, the result is a 32-bit doubleword
    A: source
    B: ax
    Product (ms 16 bits): dx
    Product (ls 16 bits): ax

## Slide 34: Multiplication instructions
source can be a register or memory location (not a constant)
Byte form
  AX=AL*source
Word form
  DX:AX=AX*source
CF/OF
  MUL
    0: upper half result 0
  IMUL
    0: if upper half is sign extension of lower half.
If ax contains 0001h and bx contains FFFFh
  mul bx; dx = 0000h ax = FFFFh
  imul bx ; dx = FFFFh ax = FFFFh (-1)
SF, ZF, AF, and PF
  Undefined

## Slide 35: More Examples
Instruction | Hex Product | DX | AX | CF/OF
MUL BX | FFFE0001 (4294836225) | FFFE (!zero) | 0001 | 1
IMUL BX | 1 | 0000 | 0001 | 0
AX=FFFFh,BX=FFFFh
AL=80h,BL=FFh
Instruction | Hex Product | AH | AL | CF/OF
MUL BL | 7F80 (32640) | 7F(!zero) | 80 | 1
IMUL BL | 0080 | 00 (no sign extension) | 80 | 1

## Slide 36: Division instructions
cbw
  convert byte to word
cwd
  convert word to doubleword
div source
  unsigned divide
idiv source
  signed divide

## Slide 37: Byte and Word Division (A/B)
When division is performed
  two results: the quotient and the remainder
  Quotient and remainder are same size as the divisor
For the byte form,
  Divisor, B: source ;Dividend , A: ax
  Quotient :al ;Remainder: ah
For the word form,
  Divisor, B: source ;Dividend , A: dx:ax
  Quotient :ax ; Remainder: dx

## Slide 38: An Example
;If dx = 0000h, ax = 0005h, and bx = FFFEh (-2)
div bx; ax = 0000h dx = 0005h
idiv bx; ax = FFFEh dx = 0001h

## Slide 39: Divide Overflow
It is possible that the quotient will be too big to fit in the specified destination (al or ax)
if the divisor is much smaller than the dividend
the program terminates and the system displays the message "Divide Overflow"

## Slide 40: Sign Extension of the Dividend
Word division
  The dividend is in dx:ax even if the actual dividend will fit in ax
  For div, dx should be cleared
  For idiv, dx should be made the sign extension of ax using cwd
e.g. -1250/7
MOV AX,-1250
CWD ; sign extend
MOV BX,7
IDIV BX

## Slide 41: Sign Extension of the Dividend
Byte division
  The dividend is in ax even if the actual dividend will fit in al
  For div, ah should be cleared
  For idiv, ah should be made the sign extension of al using cbw

## Slide 42: Logic, Shift and Rotate
Boolean Data 0 or 1
  Requires only a single bit
  0 = FALSE
  1 = TRUE
Boolean operators
  Unary: NOT
  Binary: AND, OR, XOR

## Slide 43: Logic Instructions
and destination, source
  Logical AND
  can be used to clear specific destination bits
not destination
  Logical NOT (one's complement)
or destination, source
  Logical OR
  can be used to set specific destination bits
test destination, source
  Test bits
xor destination, source
  Logical Exclusive OR
  can be used to complement specific destination bits
selectively modify the bits
in the destination using
a bit pattern (mask)

## Slide 44: Examples
To clear the sign bit of al while leaving the other bits unchanged,
  01111111b = 7Fh (mask)
  and al,F7h ;1111 0111
To set the MSB and LSB of al while preserving the other bits,
  10000001b = 81h (mask)
  or al,81h
To change the sign bit of dx,
  8000h (mask).
  xor dx,0FFFFh

## Slide 45: Examples
Converting character to decimal:
  Sub al, 30h ;Or
  Sub al, 48 ; Or
  AND ax, 000fh ;?? 0000 1111
  32h = 0011 0010
  2d = 0000 0010
How about reverse (decimal to character)??
Xor ax,ax ;ZF=1
Mov/xchg ax,0 ;ZF=unchanged

## Slide 46: The TEST instruction
TEST destination, source
  Performs AND, does not store result
  Flags are set as if the AND were executed
Example
TEST CL, 10000001b ;cl=1111 1110 (7Eh) JZ EvenAndNonNegative ;jump if ZF=1 JS Negative ; jump if SF=1 ; must be odd and positive if it gets here

## Slide 47: Bit Shifting
Slide bits in byte or word to left or right
  What happens to bit that is shifted out?
    It is copied into the CF
  What bit value is shifted in?
    SHR, SHL, SAL: =0
    SAR: =sign bit
    ROR, ROL: =bit shifted out
    RCR, RCL: =CF

## Slide 48: Left Shift Instructions
Shl
  Zeros are shifted into the rightmost bit positions
  last bit shifted out goes into CF
Effect on flags:
  SF, PF, ZF reflect the result
  AF is undefined
  CF = last bit shifted out
  OF = 1 if result changes sign on last shift
dh = 10001010, cl = 00000011
after shl dh,cl
  dh = 01010000, cf = 0
  What about of ?

## Slide 49: The SAL instruction
shl :multiply an operand by powers of 2
sal(shift arithmetic left)
  used in instances where multiplication is intended
Both instructions generate the same machine code!

## Slide 50: Rotate
Rotate Instructions Rotate Left
  rol (rotate left) shifts bits to the left
  The msb is shifted into the rightmost bit
  The cf also gets the the bit shifted out of the msb
Rotate Right
  ror (rotate right) rotates bits to the right
  the rightmost bit is shifted into the msb
  into cf

## Slide 51: Rotate through Carry
Rotate through Carry Left
  The instruction rcl shifts bits to the left
  The msb is shifted into cf
  cf is shifted into the rightmost bit
Rotate through Carry Right
  rcr rotates bits to the right
  The lsb bit is shifted into cf
  cf is shifted into the msb

## Slide 55: An example
Multiplication by 5
;Assume AX contains a number N to be multiplied by 5
MOV DX,AX ;DX=N also SHL AX,2 ;AX=4N ADD AX,DX ;AX=4N+N=5N

## Slide 56: Your turn..
Reverse a bit pattern:
Input: AL=1000 0000, Output: AL=0000 0001

## Slide 57: Thank You